## Slide 1
Networking MCQs: Q36–Q40
Given, Formula, Solution, Answer

## Slide 2
Set 1: Q36 – Frame Relay burst duration
Max burst duration?
A. 0.25 s B. 0.5 s C. 1 s D. 2 s
GIVEN
CIR = 2 Mbps
Burst size (Bc) = 1 Mb
Find: Burst time
FORMULA
Burst time = Bc ÷ CIR
SOLUTION
= 1 Mb ÷ 2 Mbps = 0.5 s
Answer: B (0.5 s)

## Slide 3
Set 2: Q37 – ATM cell size
ATM cell size?
A. 48 B. 53 C. 64 D. 128
GIVEN
Header = 5 bytes
Payload = 48 bytes
Find: Total cell size
FORMULA
Cell = Header + Payload
SOLUTION
= 5 + 48 = 53 bytes
Answer: B (53)

## Slide 4
Set 3: Q38 – MPLS label size
MPLS label size?
A. 16 bits B. 20 bits C. 24 bits D. 32 bits
GIVEN
Asked: size of the MPLS label field
Full header = 32 bits
Find: Label field size
FORMULA
Header = Label + EXP + S + TTL
SOLUTION
32 = 20 + 3 + 1 + 8, so label = 20 bits
Answer: B (20 bits)

## Slide 5
Set 4: Q39 – Virtual circuit setup
A virtual circuit requires setup of:
A. Path B. Frames C. Tokens D. Slots
GIVEN
Connection-oriented network
Data follows a fixed route
Find: What is set up first
FORMULA
Concept: works like a phone call
SOLUTION
Path is set up first, then data flows
Answer: A (Path)

## Slide 6
Set 5: Q40 – Voice per ATM cell
How many ms of voice per cell?
A. 4 B. 6 C. 8 D. 10
GIVEN
ATM payload = 48 B
Voice sample rate = 6 B/ms
Find: Time to fill one cell
FORMULA
Time = Payload ÷ Voice rate
SOLUTION
= 48 B ÷ 6 B/ms = 8 ms
Answer: C (8)

## Slide 7
Final Answer Key
Set | Question | Answer
1 | Q36 | B
2 | Q37 | B
3 | Q38 | B
4 | Q39 | A
5 | Q40 | C